## Slide 2: Overview
Part1 - Introduction
    Design Topics
      Design hierarchy
    Design Procedure
      The major design steps: specification, formulation, optimization, technology mapping, and verification
    Technology Mapping
      From AND, OR, and NOT to other gate types
  Decoders
Part 2
  Encoders
  Multiplexers
  Binary Adders

## Slide 3: Combinational Circuits
A combinational logic circuit has:
  A set of m Boolean inputs,
  A set of n Boolean outputs, and
  n switching functions, each mapping the 2m input combinations to an output such that the current output depends only on the current input values
A block diagram:
m Boolean Inputs
n Boolean Outputs
Combinatorial
Logic
Circuit

## Slide 4: Decoding
Decoding - the conversion of an n-bit input code to an m-bit output code with n £ m £ 2n such that each valid code word produces a unique output code
Circuits that perform decoding are called decoders
Here, functional blocks for decoding are
  called n-to-m line decoders, where m £ 2n, and
  generate 2n (or fewer) minterms for the n input variables

## Slide 5: Decoder Examples
1-to-2-Line Decoder
2-to-4-Line Decoder
Note that the 2-4-line made up of 2 1-to-2- line decoders and 4 AND gates.

## Slide 6: Decoder with Enable
In general, attach m-enabling circuits to the outputs
See truth table below for function
  Note use of X’s to denote both 0 and 1
  Combination containing two X’s represent four binary combinations
Alternatively, can be viewed as distributing value of signal EN to 1 of 4 outputs
In this case, called a demultiplexer

## Slide 7: 2-to-4 Decoder Diagram

## Slide 8: NAND Only

## Slide 9: Decoder Expansion
General procedure given in book for any decoder with n inputs and 2n outputs.
This procedure builds a decoder backward from the outputs.
The output AND gates are driven by two decoders with their numbers of inputs either equal or differing by 1.
These decoders are then designed using the same procedure until 2-to-1-line decoders are reached.
The procedure can be modified to apply to decoders with the number of outputs ≠ 2n

## Slide 10: 3-to-8-line decoder (without enable)
Consider a 3-to-8-line decoder (without enabler)
A2 | A1 | A0 | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7
0 | 0 | 0 | 1 |  |  |  |  |  |  | 
0 | 0 | 1 |  | 1 |  |  |  |  |  | 
0 | 1 | 0 |  |  | 1 |  |  |  |  | 
0 | 1 | 1 |  |  |  | 1 |  |  |  | 
1 | 0 | 0 |  |  |  |  | 1 |  |  | 
1 | 0 | 1 |  |  |  |  |  | 1 |  | 
1 | 1 | 0 |  |  |  |  |  |  | 1 | 
1 | 1 | 1 |  |  |  |  |  |  |  | 1

## Slide 11: 3-to-8-line Decoder Implementation

## Slide 12: Easier way by Expansion
Decoder expansion
  Combine two or more small decoders with enable inputs to form a larger decoder
3-to-8-line decoder constructed from two 2-to-4-line decoders
    The MSB is connected to the enable inputs
    if A2=0, upper is enabled; if A2=1, lower is enabled.

## Slide 13: Expansion

## Slide 14: Combinational Circuit Design with Decoders
Combinational circuit implementation with decoders
  A decoder provide 2n minterms of n input variables
  Since any Boolean function can be expressed as a sum of minterms, one can use a decoder and external OR gates to implement any combinational function.

## Slide 15: Combinational Circuit Design with Decoders
Realize F (X,Y,Z) = Σ (1, 4, 7) with a decoder:

## Slide 16: Decoder Implementation of a Full Adder
Truth Table: We have two outputs, called S, which stands for sum, and C, which stands for carry. Both sum and carry are functions of X, Y, and Z.

## Slide 17: Decoder Implementation of a Full Adder
The output functions S & C can be expressed in sum-of-minterms forms as follows:
S is implemented by taking minterms 1, 2, 4, and 7 and the OR gates forms the logical sum of minterm for S
Similarly, carry C is implemented by taking logical sum of minterms 3, 5, 6, and 7 from the same decoder

## Slide 18: Spring 2024 Question 6

## Slide 19: Spring 2024 Question 6

## Slide 20: Fall 2023 Question 5

## Slide 21: Fall 2023 Question 5

## Slide 22: Thank You