## Slide 2: Overview
Part1 - Introduction
    Design Topics
      Design hierarchy
    Design Procedure
      The major design steps: specification, formulation, optimization, technology mapping, and verification
    Technology Mapping
      From AND, OR, and NOT to other gate types
  Decoders
Part 2
  Encoders
  Multiplexers
  Binary Adders

## Slide 3: Encoding
Encoding - the opposite of decoding - the conversion of an m-bit input code to a n-bit output code with n £ m £ 2n such that each valid code word produces a unique output code
Circuits that perform encoding are called encoders
An encoder has 2n (or fewer) input lines and n output lines which generate the binary code corresponding to the input values
Typically, an encoder converts a code containing exactly one bit that is 1 to a binary code corres-ponding to the position in which the 1 appears.

## Slide 4: Encoder

## Slide 5: Encoder Example
A decimal-to-BCD encoder
  Inputs: 10 bits corresponding to decimal digits 0 through 9, (D0, …, D9)
  Outputs: 4 bits with BCD codes
  Function: If input bit Di is a 1, then the output (A3, A2, A1, A0) is the BCD code for i,
The truth table could be formed, but alternatively, the equations for each of the four outputs can be obtained directly.

## Slide 6: Decimal-to-BCD encoder

## Slide 7: Encoder Example (continued)
Input Di is a term in equation Aj if bit Aj is 1 in the binary value for i.
Equations:
  A3 = D8 + D9
  A2 = D4 + D5 + D6 + D7
  A1 = D2 + D3 + D6 + D7
  A0 = D1 + D3 + D5 + D7 + D9
F1 = D6 + D7 can be extracted from A2 and A1 Is there any cost saving?
Notes: No. The total gate input cost remains the same.

## Slide 8: Encoder Example (continued)
  A3 = D8 + D9
  A2 = D4 + D5 + D6 + D7
  A1 = D2 + D3 + D6 + D7
  A0 = D1 + D3 + D5 + D7 + D9

## Slide 9: Spring 2024 Question 5

## Slide 10: Spring 2024 Question 5

## Slide 11: Fall 2023 Question 6

## Slide 12: Fall 2023 Question 6

## Slide 13: Fall 2023 Question 6

## Slide 14: Priority Encoder
If more than one input value is 1, then the encoder just designed does not work.
One encoder that can accept all possible combinations of input values and produce a meaningful result is a priority encoder.
Among the 1s that appear, it selects the most significant input position (or the least significant input position) containing a 1 and responds with the corresponding binary code for that position.

## Slide 15: Priority Encoder Example
Priority encoder with 5 inputs (D4, D3, D2, D1, D0) - highest priority to most significant 1 present - Code outputs A2, A1, A0 and V where V indicates at least one 1 present.
Xs in input part of table represent 0 or 1; thus table entries correspond to product terms instead of minterms. The column on the left shows that all 32 minterms are present in the product terms in the table
No. of Min-terms/Row | Inputs |  |  |  |  | Outputs |  |  | 
 | D4 | D3 | D2 | D1 | D0 | A2 | A1 | A0 | V
1 | 0 | 0 | 0 | 0 | 0 | X | X | X | 0
1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
2 | 0 | 0 | 0 | 1 | X | 0 | 0 | 1 | 1
4 | 0 | 0 | 1 | X | X | 0 | 1 | 0 | 1
8 | 0 | 1 | X | X | X | 0 | 1 | 1 | 1
16 | 1 | X | X | X | X | 1 | 0 | 0 | 1
Notes: Go over table explaining how entries were obtained, particularly those containing Xs

## Slide 16: Priority Encoder Example (continued)
Could use a K-map to get equations, but can be read directly from table and manually optimized if careful:
  A2 = D4
  A1 = D3 + D2 = F1, F1 = (D3 + D2)
  A0 = D3 + D1 = (D3 + D1)
  V = D4 + F1 + D1 + D0
D4
D3
D4
D4
D4
D3
D4
D2
D4
D2

## Slide 17: Spring 2024 Question 4

## Slide 18: Spring 2024 Question 4

## Slide 19: Spring 2024 Question 4

## Slide 20: Spring 2024 Question 4

## Slide 21: Spring 2024 Question 4

## Slide 22: Spring 2024 Question 4

## Slide 23: Fall 2023 Question 4

## Slide 24: Fall 2023 Question 4

## Slide 25: Fall 2023 Question 4

## Slide 26: Fall 2023 Question 4

## Slide 27: Selecting
Selecting of data or information is a critical function in digital systems and computers
Circuits that perform selecting have:
  A set of information inputs from which the selection is made
  A single output
  A set of control lines for making the selection
Logic circuits that perform selecting are called multiplexers
Selecting can also be done by three-state logic or transmission gates

## Slide 28: Multiplexers
A multiplexer selects information from an input line and directs the information to an output line
A typical multiplexer has n control inputs (Sn - 1, … S0) called selection inputs, 2n information inputs (I2n - 1, … I0), and one output Y
A multiplexer can be designed to have m information inputs with m < 2n as well as n selection inputs

## Slide 29: 4-to-1-line Multiplexer

## Slide 30: 2-to-1-Line Multiplexer
Since 2 = 21, n = 1
Selection variable S:
  S = 0 selects input I0
  S = 1 selects input I1
The equation:
Y = I0 + SI1
The circuit:
S
S | Y
0 | I0
1 | I1

## Slide 31: 2-to-1-Line Multiplexer (continued)
Note the regions of the multiplexer circuit shown:
  1-to-2-line Decoder
  2 Enabling circuits
  2-input OR gate
To obtain a basis for multiplexer expansion, we combine the Enabling circuits and OR gate into a 2 ´ 2 AND-OR circuit:
  1-to-2-line decoder
  2 ´ 2 AND-OR

## Slide 32: Example: 4-to-1-line Multiplexer
2-to-22-line decoder
22 ´ 2 AND-OR
Y = (S1 S0) I0 + (S1 S0) I1 + (S1 S0) I2 + (S1 S0) I3

## Slide 33: Combinational Function Implementation
Alternative implementation techniques:
  Decoders and OR gates
  Multiplexers (and inverter)

## Slide 34: Combinational Function Implementation
F(x,y,z) = Σ(1,2,6,7) using 4-to-1 multiplexer.
Connect the variables x and y to the selection inputs S1, and S0. The inputs of the multiplexers can be obtained from the truth table as shown below.

## Slide 35: F(A, B, C, D) = Σ(2, 3, 5, 7, 10, 11, 15)

## Slide 36: Spring 2024 Question 7

## Slide 37: Fall 2023 Question 7

## Slide 38: Fall 2023 Question 7

## Slide 39: Thank You