## Slide 2: Counters
Counters are sequential circuits which "count" through a specific state sequence. They can count up, count down, or count through other fixed sequences. Two distinct types are in common usage:
Ripple Counters
  Clock is connected to the flip-flop clock input on the LSB bit flip-flop
  For all other bits, a flip-flop output is connected to the clock input, thus circuit is not truly synchronous
  Output change is delayed more for each bit toward the MSB.
  Resurgent because of low power consumption
Synchronous Counters
  Clock is directly connected to the flip-flop clock inputs
  Logic is used to implement the desired state sequencing

## Slide 3: Ripple Counter
How does it work?
  When there is a positive edge on the clock input of A, A complements
  The clock input for flip- flop B is the complemented output of flip-flop A
  When flip A changes from 1 to 0, there is a positive edge on the clock input of B causing B to complement
Reset
Clock
D
D
CR
CR
B
A
CP
B
A
0
1
2
3
0
1

## Slide 4: Ripple Counter (continued)
These circuits are called ripple counters because each edge sensitive transition (positive in the example) causes a change in the next flip-flop’s state.
The changes “ripple” upward through the chain of flip-flops, i. e., each transition occurs after a clock-to-output delay from the stage before.

## Slide 5: Ripple Counter: 4-bit Upward Counter
Remember J-K toggles when both J and K are ‘1’
The bubble on the clock means negative-edge triggered
When Q0 goes from ‘1’ to ‘0’ (as if a negative-edge has been triggered to clock of Q1), Q1 toggles
When Q1 goes from ‘1’ to ‘0’, Q2 toggles
When Q2 goes from ‘1’ to ‘0’, Q3 toggles

## Slide 6: Ripple Counter: 4-bit Upward Counter
When Q0 goes from ‘1’ to ‘0’ (as if a negative-edge has been triggered to clock of Q1), Q1 toggles
When Q1 goes from ‘1’ to ‘0’, Q2 toggles
When Q2 goes from ‘1’ to ‘0’, Q3 toggles
What about the last sequence: how it goes from ‘1111’ to ‘0000’?

## Slide 7: Synchronous Counters
To eliminate the "ripple" effects, use a common clock for each flip-flop and a combinational circuit to generate the next state.
For an up-counter, use an incrementer =>
D3
Q3
D2
Q2
D1
Q1
D0
Q0
Clock
Incre-menter
A3
A2
A1
A0
S3
S2
S1
S0

## Slide 8: 4-bit Synchronous Counter with J-K

## Slide 9: K-Maps

## Slide 10: Equations
EN has been added to control the operation of the counter
This relations could be generalized
A Carry Output (CO) has been added so that the counter could be extended to more stages
The implementation might be positive/negative edge triggered

## Slide 11: Logic Diagram

## Slide 12: Arbitrary Counter: Problem Statement
Design an arbitrary counter that repeatedly follows the following sequence:
0, 1, 2, 4, 5, 6, 0, 1, 2, 4, 5, 6, 0. . .
If accidentally the counter starts with ‘3’, it should move to ‘4’ in the next step
If accidentally the counter starts with ‘7’, it should move to ‘0’ in the next step

## Slide 13: Arbitrary Counter: State Diagram

## Slide 14: Arbitrary Counter: State Table

## Slide 15: Arbitrary Counter: Logic Diagram

## Slide 16: Spring 2024 Question 2

## Slide 17: Spring 2024 Question 2

## Slide 18: Spring 2024 Question 2

## Slide 19: Spring 2024 Question 2

## Slide 20: Spring 2024 Question 2

## Slide 21: Fall 2023 Question 2

## Slide 22: Fall 2023 Question 2

## Slide 23: Fall 2023 Question 2

## Slide 24: Fall 2023 Question 2

## Slide 25: Fall 2023 Question 2

## Slide 26: Fall 2023 Question 2

## Slide 27: Thank You