## Slide 2: Registers
Register – a collection of binary storage elements
In theory, a register is sequential logic which can be defined by a state table
More often think of a register as storing a vector of binary values
Frequently used to perform simple data storage and data movement and processing operations

## Slide 3: 4-Bit Register
Clear goes to R
We put ‘1’ all the time
Put ‘0’ if want to clear the values

## Slide 4: Register with Parallel Load
If data is not changed no need to trigger the clock
Clock inputs = C inputs
When Load = 1, register is clocked normally, new data is loaded
Note, clock pulses arrive periodically, Load determines if new data would be loaded or not

## Slide 5: Shift Registers
Shift Registers move data laterally within the register toward its MSB or LSB position
In the simplest case, the shift register is simply a set of D flip-flops connected in a row like this:
Data input, In, is called a serial input or the shift right input.
Data output, Out, is often called the serial output.
The vector (A, B, C, Out) is called the parallel output.

## Slide 6: Shift Registers (continued)
The behavior of the serial shift register is given in the listing on the lower right
T0 is the register state just before the first clock pulse occurs
T1 is after the first pulse and before the second.
Initially unknown states are denoted by “?”
Complete the last three rows of the table
D
Q
D
Q
D
Q
D
Q
In
Clock CP
A
B
C
Out
CP
In
A
B
C
Out
T0
0
?
?
?
?
T1
1
0
?
?
?
T2
1
1
0
?
?
T3
0
1
1
0
?
T4
1
T5
1
T6
1
Notes: ROW T4: 10110
Row T5: 11011
Row T6: 11101

## Slide 7: Parallel Load Shift Registers
By adding a mux between each shift register stage, data can be shifted or loaded
If SHIFT is low, A and B are replaced by the data on DA and DB lines, else data shifts right on each clock.
By adding more bits, we can make n-bit parallel load shift registers.
A parallel load shift register with an added “hold” operation that stores data unchanged is given in Figure 7-10 of the text.
D
Q
D
Q
A
B
CP
SHIFT
IN
DA
DB

## Slide 8: Universal Shift Register
Construct a 3-bit register with the functions given in the function table below

## Slide 9: Universal Shift Register
Construct a 3-bit register with the functions given in the function table below

## Slide 10: Spring 2024 Question 3

## Slide 11: Spring 2024 Question 3

## Slide 12: Fall 2023 Question 3

## Slide 13: Fall 2023 Question 3

## Slide 14: Thank You